## Slide 1: Status of the EIC R&D @ UVa
Kondo Gnanvo
EIC Weekly Meeting, Oct 30, 2017

## Slide 2: Charging up of Cr-GEM prototype
Cr-GEM foils from CERN so far have a grid of Cu strip (pitch 2 mm, width ~ 100 µm)
This is originally to ensure good electrical contact even when we have a local problem Cr layer
Some charging up is observed at the beginning of each x-ray test.
Gain is more pronounced around the grid defined by the Cu strips, This is observed at the operating HV for x-ray (equivalent ~ 1000 to 2000 for a standard triple GEM)
After a long exposure to x-ray (more ~ day) then the gain become more uniform
  Cu strips are not visible anymore and the relative gain variation is far less pronounced
The phenomenon is repeatable ⇨ if I switch everything off for a day and restart the test, I reproduced the same effect
Rui thinks that it might have to do with the larger holes size of the Cr after the Cu is removed
  This is something we should be able to see with the optical scanning at Temple U or the SEM at CERN

## Slide 3: Charging up of Cr-GEM prototype
Similar effect was observed when working at a higher gain (~5000) and at higher rate
But did not result in any permanent alteration of the Cr-GEM foils because when the testes is repeated at the lower gain and lower rate, we can go back to a more uniform gain distribution
Here again this is clearly a charging up effect caused by the Cu-Strip
I need to repeat these tests by changing parameters one by one and also by changing only one variable at the time

## Slide 4: Summary and R&D plans for Cr-GEM foils
Current Cr-GEM prototype indicate that there is no aging / radiation damage with the foils at operating gain
It is also very stable moderate rate ⇨ x-ray tests were done at a rate that is probably an order of magnitude higher than what is expected for EIC in the forward region
But charging up effect is observed at the beginning of x-ray test and also at very high gain and high particle rate
Trip to Temple U during the week of Nov 15 to perform the optical scanning of Cr-GEMs foils (damaged foil and good foil from old batch + good foil from the newer batch)
  Goal is to map the damage foil and try to confirm the removal of Cr-layer
  Make hole size analysis to see whether Cr-GEM hole size can explain the charging up effect that we are observing
Early December ⇨ Samples of the same foils will be shipped to CERN for the SEM measurement. RD51 (namely Eraldo) will be helping with the logistics and administrative part of the test
  This should complement the optical inspection and reveal local information of the holes geometry
  Hole size and geometry at the boundary between Cr holes and Cu-strip
Near future ⇨ pursue the x-ray studies with plain Cr-GEM (with no Cu grid) and compared the Cu-grid Cr-GEMs
With the joint simulation studies together with Florida Tech and help from Alexander at BNL we should be able to have a full picture of the Cr-GEM for EIC

## Slide 5: Large FT GEM: U-V strip readout board received from CERN
2D U-V readout layer a la COMPASS, Excellent spatial resolution
No metallized vias to pick up bottom strips signal ⇨Thin Cu layer
All FE electronics read out all on the outer radius of the chamber
Top strip
Bottom strip
Kapton
Components of the zebra connection

## Slide 6: Summary and R&D plans for large FT GEM prototype
We already have had so far (last two years):
  The GEM foils
  The U-V strips R/O board
  The Zebra-to-Panasonic adapter boards
We are still waiting for and need to get ready in the next few months:
  The support frames, we need to find ~ 6$K if we go the our idea or splitting the production in two parts low cost local production for the outer frames (~ 1k$) and production at RESARM Belgium of the inner frames (5$k)
  Order of Zebra strips already processed, waiting for delivery
  We need to refurbish existing assembly plates ad accessories in the clean room to accommodate the EIC design
Plan is to built the prototype built early 2018 and be ready for Test beam probably in July 2018
We started the discussion with FTBF (e-mail exchange with Mandy Rominsky) to schedule FLYSUB test beam
  Tentative date is July 4 to July 24 2018 (best time that we can be primary users all the time and it also more convenient for Marcus etc …) but waiting for December confirmation from FTBF
  So far Florida Tech and UVa are onboard (maybe eRD3 will also bring a chamber) but we would like a larger community ….